## Slide 1: Exercise Pipeline Flow Simulation

## Slide 2: Goal: To Calculate the BHP (Brake HorsePower) to transmit Oil over a Pipeline

## Slide 3: Situation: You are responsible for a section of pipeline (1600 feet, 8” Case Iron pipe)

## Slide 5: Oil of Different Densities Flows Through the Pipe Section

## Slide 6: Four Different vendors are leasing your pipe
You choose one vendor per day.

## Slide 7: You use a Pump to transmit the Oil

## Slide 8: You must maintain a Volumetric Flow Rate: Q = 0.09457 cubic m/sec

## Slide 9: Head Loss = Hf = 25.51 metres

## Slide 10: Mass Flow Rate = Oil Denisty * Q = rho * 0.09457 m^3/sec
Rho is oil density. (given to you)
Units of Mass flow rate = m-dot = Kg/s

## Slide 11: Power = Mass Flow Rate * Hf * g
Power is measured in Watts
Hf = Head Loss
g = Acceleration due to gravity (9.8 m/s^2)

## Slide 12: HorsePower to Watts 1 Watt = 0.00134102 HPs

## Slide 13: BHP = HP / Efficiency

## Slide 14
 | Oil Density (Kg/m^3) | Probability of Using Vendor
Vendor 1 | 900 | 60%
Vendor 2 | 680 | 20%
Vendor 3 | 1000 | 10%
Vendor 4 | 775 | 10%

## Slide 15
The 4 Vendors have 4 different oil densities

## Slide 16: Pump Efficiency is Uniformly Distributed between 75% - 80%

## Slide 17: Task 1: Make 1 million replications of using the different oils and calculate the BHP for each trial

## Slide 18: Task 1: In each trial, choose one Vendor according to the probability in the table

## Slide 19: Task 1: In each trial, choose the PUMP EFFICIENCY Uniformly between 75%-80%

## Slide 20: Task 1: Create a Sim_1_results Data Frame. In it, Store the following: Vendor, Density, Efficiency, HP and BHP

## Slide 21: Task 1: Why Vendor Takes up the Most power? The Least Power?

## Slide 22: Task 1: What is the mean BHP needed?

## Slide 23: Task 1: Plot a HISTOGRAM of BHP

## Slide 24: Task 1: Plot the simulated Pump Efficiency (x-axis) vs the BHP Required (y-axis)

## Slide 25: Task 2: If you Company buys a NEW PUMP with a fixed 85% efficiency what is the % benefit in BHP? BHP Task1 vs BHP_Simulation Task 2

## Slide 26: Reference
https://www.convertunits.com/from/kg-m/s/to/horsepower+[international]
http://www.discoverhover.org/infoinstructors/conversion.htm